## Slide 1
REAL VS DECOY FILTER 1/4
Two Depth Cues from Detector Boxes
Outer ring (+50% box pad): median valid depth
Detector box: depth frame within 50 ms
Central half: 25th percentile of valid depth
1. Projected box height (m)
Estimates the metric height represented by the detection box.
2. Relative depth contrast
Compares the ring depth with the central estimate.

## Slide 2
REAL VS DECOY FILTER 2/4
Threshold Selection and Decision Rule
STEP 01
Reference Match
Match a detector box by its centre inside a reference box.
STEP 02
Three Time Blocks
Fit on two blocks, then check the held-out block.
STEP 03
Threshold Search
Require real TPR ≥ 0.75, then minimize accepted decoys.
STEP 04
Final Eval Fit
Fit on all eval labels and save the thresholds for test.
SAVED RULE (FINAL FIT ON EVAL DATA)
height ≥ 0.5554 m AND contrast ≥ 0.1922
REAL if both pass
Both cues must be valid

## Slide 3
REAL VS DECOY FILTER 3/4
Eval Depth Cues and Held-Out Results
Matched candidates with both depth cues
Relative contrast
0
0.4
0.8
1.2
1.6
-0.5
0.5
1.5
2.5
3.5
4.5
5.5
Projected box height (m)
Real (n=140)
Decoy (n=106)
Held-out check
Fit on two blocks, check the third.
Block
Real accepted
Decoys accepted
1
31 / 33
0 / 53
2
33 / 33
1 / 55
3
33 / 33
1 / 52
Total
97 / 99
2 / 160
Counts are labeled occurrences per frame.
Why did two decoys pass?
Each held-out block uses cutoffs fitted on the other two. The final fit on all eval data rejects both.
Accept-all baseline
99 / 99 real, 93 / 160 decoys
TPR 1.000, FPR 0.581
Held-out filter
97 / 99 real, 2 / 160 decoys
TPR 0.980, FPR 0.013

## Slide 4
REAL VS DECOY FILTER 4/4
Test Examples and Boundary Cases
Accepted real object
Rejected printed decoys
Real object rejected
Height 0.955 m, contrast 0.098 < 0.192
Mixed or missing depth near a box can change either cue.
Test: 2 real missed, 0 / 103 decoys accepted